## Slide 1: Acrysion with Airbrush
Twitter ：@kazz185
Blog ：https://kazz185.work

## Slide 2: Painting Environment for Acrysion（1/2）
My Working Room
  Room in th Attic
  It's small and dry
Compressor
  MR.LINEAR COMPRESSOR L5/PS289 AIRBRUSH
    A full set of Mr.LINEAR COMPRESSOR L5
    with airbrush Mr.PROCONBOY WA PLATINUM(0.3MM)
    VER.2 and Mr.AIR REGULATOR Mk-Ⅳ.
Airbrush
  MR.PROCON BOY LWA TRIGGER TYPE (0.5MM)
  +PS-290G
    ADDITIONAL GRIP FOR PS290
Painting Booth
  D.I.Y
    Ventilation fan
      FY-24BM6K （Panasonic）
      Quiet fan(38.5dB)
    https://kazz185.work/post/10/
Drying booth
  Tableware dryer (By Yamazen)

## Slide 3: Painting Environment for Acrysion（2/2）
Thermo-Hygrometer
  EX-2717（empex）
Kitchen scale
  KJ-212（TANITA）
    Can measure up to 0.1g
    With tare function
Acrysion Thinner
  Acrysion thinner for Airbrush
  This is recommeneded Not only for airbrush
  but also brush painting.
  From now on, simply referred to as “Acrysion Thinner”
Green Tee Filter (Tea Bag)
  This is the most important item for airbrush painting
  with Acrysion
  Cover the cup, pour in to filter Acrysion.
Others
  Using Paint Stirrer (TAMIYA)

## Slide 4: About dilution with an airbrush（1/2）
About dilution
  Shake Acrysion thinner WELL
  It is normal that it is cloudy in white.
Acrysion Series (N-xx)
  Acrysion to Thinner ratio is 1:0.84
    However, it is about 0.8-0.9
    Ex) Acrysion is 0.5g and Thinner is 0.42g
      First, put 0.5g of Acrysion in a paper cup.
      Next, add Thinner until it reaches 0.9g.
  Acrysion Clear Series（N-20,N-30）
    Acrysion to Thinner ratio is 1:2 (and more ?)
    During verification (Sorry)

## Slide 5: About dilution with an airbrush（2/2）
Acrysion BaseColor Series (BN-xx)
    Acrysion to Thinner ratio is 1:1.1
      Base White (BN-1) is 1:1.1
      Base Gray (BN-2) is 1:1.2
      Dilution is changed by color

## Slide 6: Painting with airbrush and air pressure （1/2）
Filter before blowing with an airbrush
  When you open and close the bottle, paint debris that has adhered to the inside of the lid will enter the bottle.
  This is one of the causes of clogging.
    Another cause is a High Pressure, I think.
  It is a mixture of metallic blue and metallic red.
    Can you see the red and blue pieces?
  Mix well to scoop the bottom of the bottle
Low Pressure（0.03MPa）
  High-pressure blowing accelerates drying
  This is the cause of clogging
  So, You can paint well with L5
Repeat spraying and drying
  The amount of paint is adjusted as follows
    PS290 Needle Stopper Possion
    From the fully occupied state to the one-lap (330°?) loose state
View from behind
330°

## Slide 7: Painting with airbrush and air pressure （2/2）
“Gargle” from time to time
  The airbrush, not YOU
  Loosen the nozzle and let the air flow backwards
  Metallic paint easily precipitates
Uploading video to YouTube
  My Channel
    https://www.youtube.com/channel/UC32cECtyWwPM_kXqcSzQwIA/
  Contents
    How to Dilution
      https://youtu.be/DA5-EkQoN-c
    Acrysion BaseColor with AirBrash
      https://youtu.be/j-8x_5SbuKo